(X-Xc)^{2} - (Z-Zc)^{2} = ({R} over {h})^2 (h - Y + Yc)^2
Equation 1: Every point on cone must satisfy this equation.

Figure 5: Diagram illustrating the location of each point.

Equation 2: Ray equations.

Figure 7: Image demonstrating Refraction (Scratchpixel 2014)
X = Xo + d_x * t
Y = Yo + d_y * t
Z = Zo + d_z * t
COSC363 Assignment 2: Ray Tracing
Harry Dobbs 89030703

# Overview:
A ray tracing algorithm has been implemented to create a realistic scene. The scene includes a wide variety of shapes and effects. The scene accurately utiilizes features such as transparency, refraction, shadows, rotation, reflection,textures and specular highlights. These features combined with the use of various shapes create a visually spectacular scene. Fog is turned on by pressing the key ‘f’. Fog is turned off by pressing the key ‘c’. There is a delay when switching between the two states.

Figure 2: Ray tracing scene with fog turned off

Figure 1: Ray tracing scene with fog turned on.

# Standard Features (9 marks):
- Contains one light source aswell as diffuse, and specular reflections generated by the source.
- Contains shadows for every object. Transparent objects create a lighter shadow.
- The scene contains one large blue reflective sphere.
- The scene contains two boxes. One is skewed and one is regular.
- The scene contains a chequerd floor.
# Additional Features (7-9 marks):
## Primitive Cone (1 mark) :
To be able to display a cone within my assignment, each ray must be able to calculate:
- If it has intersected with the cone
- The normal vector at the point of intersection
These two requirements were constructed as functions. To be able to implement these fucntions, geometric equations were required. The equations for a cone, and cylinder accompained with labelled diagrams (Figure 5) were provided in the lecture notes (Mukundan ,2019). The points of intersection are obtained by substituing the ray equations (Equation 2) into the general point equation (Equation 1). The resulting equation is then solved for t. An issue I had with the original implementation was that a second cone was generated on top of the cone I wanted to display (Figure 3). This issue was resolved by substituing the value of t into the Y ray equation (Equation 2) and ensuring the height was less then the summation of the cone centre plus the height of the cone (Figure 4). A similar method was used to constrain the minimum height of the cone (Figure 4).

Figure 3: Image of incorrectly implemented cone.

Figure 4: Equation implementation to ensure cone in contained with certain values of Y.

Figure 6: Image Capture of Cone Implementation

## Primitive Cylinder (1 mark) :
## Transparent Object (1 mark) :
When an object is transparent an additional ray in generated in the same direction as the ray that intersected with the transparent object. However this ray’s origin is on the other side of the transparent object. The pixel colour that is displayed to us is a result of the transparent object multiplied by some transmission factor summed with the colour returned from the additional ray. An issue I had with the implementation is that sometimes the origin of the additional ray is the at the same point the original ray contacts the object (as shown by red arrow in Drawing 1) as opposed to being on the other side of the object (as shown by blue arrow in Drawing 1) . This issue was relatively to simple to resolve and once resolved the transparent object edges looked cleaner.

Drawing 1: An Illustration demonstrating two scenarios when dealing with transparent objects.

## Refraction of Light (1 mark) :
Refraction occurs when light travels through a transparent medium to another medium and the light is bent around a boundary. Light travels at different speeds in different mediums. Different mediums have different indexs of refraction. GLM has a function that takes the direction vector, normal vector and the ratio refractive indicies. This function will return a vector that is pointed in the correct direction. This vector is then traced.

## Rotation or Shear Transformation (1-2 mark) :
## Non-planar Object Texturing Cone (1 mark) :
## Fog Implementation (1-2 mark) :

# References :

Dr. R. Mukundan . (2019) . Computer Graphics COSC363 Lec09_RayTracing [PowerPoint Slides]. Retrieved from https://learn.canterbury.ac.nz/mod/resource/view.php?id=803416
Scratchapixel. (2014, August 15). Retrieved May 30, 2019, from https://www.scratchapixel.com/lessons/3d-basic-rendering/introduction-to-shading/reflection-refraction-fresnel